## Slide 1: ASTM E2893-16 Greener Cleanup Self-Declaration at Marine Corps Base Camp Lejeune
June 28, 2018
CH2M is now Jacobs
Monica Fulkerson, P.E., ENV SP, Project Manager, Jacobs
Betsy Collins, P.E., LEED Green Associate, Project Engineer, Jacobs
Paul Favara, P.E., Senior Technical Consultant, Jacobs
David Cleland, P.G., Remedial Project Manager, NAVFAC
Charity Delaney, P.E., Environmental Management Division, Marine Corps Base Camp Lejeune

## Slide 2: Agenda
Review ASTM E2893-16: Standard Guide for Greener Cleanups Process
Present MCB Camp Lejeune Self-Declaration
Discuss Benefits of Self-Declaration
Agenda
Process
Implementation
Key Take-Aways

## Slide 3: What is the Standard Guide for Greener Cleanups?

## Slide 4: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
The act of cleanup creates its own environmental impacts
  Energy requirements
  Air pollution
  Water use
  Material production/waste disposal
  Land and ecosystem impacts
Standard provides process for identifying, evaluating, incorporating, and documenting best management practices (BMPs) during cleanup
Agenda
Process
Implementation
Key Take-Aways

## Slide 5: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
Agenda
Process
Implementation
Key Take-Aways

## Slide 6: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
Opportunity Assessment
  Review 114 listed BMPs
  Organized by category
    Buildings
    Materials
    Power
    Residual Waste
    Vehicles
  Identify applicable BMPs
Agenda
Process
Implementation
Key Take-Aways

## Slide 7: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
Agenda
Process
Implementation
Key Take-Aways
Prioritization
  Based on ability to reduce footprint
    Low
    Medium
    High
  Professional judgement
    Supported by quantitative evaluation, if appropriate

## Slide 8: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
Agenda
Process
Implementation
Key Take-Aways
Selection
  Based on potential footprint reductions
  Considers typical comparison criteria
  Reasons for exclusion
    Technology screened out
    Inability to meet project requirements
    Negative effect on core element
    Less impact with standard approach

## Slide 9: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
Agenda
Process
Implementation
Key Take-Aways

## Slide 10: Overview of ASTM E2893-16: Standard Guide for Greener Cleanups
BMP Process
Opportunity Assessment
Prioritization
Selection
Implementation
Documentation
  For each cleanup phase
  Public submittal
Agenda
Process
Implementation
Key Take-Aways

## Slide 11
Agenda
Process
Implementation
Key Take-Aways

## Slide 12: Marine Corps Base Camp Lejeune’s Self-Declaration

## Slide 13: MCB Camp Lejeune Greener Cleanup Self-Declaration
MCB Camp Lejeune
  Mission: Maintain combat-ready warfighters for expeditionary deployment
  Second largest Marine Corps Base in the USA (approximately 236 square miles)
  49 active environmental sites
Agenda
Process
Implementation
Key Take-Aways

## Slide 14: MCB Camp Lejeune Greener Cleanup Self-Declaration
Self-declaration completed in 2017
  BMP evaluation
    29 potentially applicable
    18 implemented
    2 user-defined
  Complemented strategy to achieve remedy objectives
  All phases of site work
Holland et al, 2011

## Slide 15: Project Highlights

## Slide 16: Solar Powered Subgrade Biogeochemical Reactor
Applicable BMPs
  Biobased and non-refined materials (locally sourced mulch and soybean oil)
  Uncontaminated site soil for backfill
  Solar powered pump
Impacts
  Reduced landfill waste and greenhouse gas emissions
  Maximized use of renewable energy
  Reduced concentrations in source area and potential time to site closure
Agenda
Process
Implementation
Key Take-Aways

## Slide 17: Air Sparging Remedial Actions
Applicable BMP
  Set milestones to system shut down
  Equipment reuse
Impacts
  Savings of ~800,000 kilowatt hours per system per year per system
    Reduced cost and GHG emissions associated with electricity production
  Avoided O&M vehicle travel
Agenda
Process
Implementation
Key Take-Aways

## Slide 18: Long Term Monitoring Program
Applicable BMPs
  No purge technology, 300 wells/year
  Optimized well network and utilized existing wells
Impacts
  Minimized waste management
    Avoided ~1,500 gallons aqueous waste/year
    Eliminated need for ~15,000 feet of tubing/year
  Reduced greenhouse gas emissions related to transportation
  Reduced time and cost
    ~600 hours or $32,000/year
Agenda
Process
Implementation
Key Take-Aways

## Slide 19: Sitewise Analysis
Remedy Selection
  Compare alternatives in terms of a consistent set of sustainability metrics
  Conducted at 8 sites
Remedy Implementation
  Identifies opportunities to reduce footprint during design
Agenda
Process
Implementation
Key Take-Aways
AS
ISCO
ERD
Construction
Operations
Monitoring
Total Energy Used - ISCO

## Slide 20: Why Self-Declare?

## Slide 21: Benefits to Self-Declaration
Get recognition for BMPs already being applied at sites
Optimize existing remedies to reduce time, cost, and environmental impacts of cleanup
Minimize environmental impacts for future cleanup actions
Trigger “The Virtuous Cycle”
Agenda
Process
Implementation
Key Take-Aways

## Slide 22: Conclusions
Agenda
Process
Implementation
Key Take-Aways
ASTM E2893-16: Standard Guide for Greener Cleanups Process
  A useful tool to document successes
Self-declaration at MCB Camp Lejeune
  Documented past successes
  Will continue to utilize BMPs moving forward
Establish a culture of green sustainable remediation
  Trigger the virtuous cycle
ASTM International

## Slide 23: Thank you!
Monica L. Fulkerson, P.E., ENV SP
Notes: With that, I thank you for your time and attention and welcome any questions.