## Slide 1: Industry Perspective on Greener Cleanups PHARMACIA & UPJOHN COMPANY LLC Greener Cleanup Case Study
USEPA Clu-In Webinar
September 28, 2016

## Slide 2: Presentation Outline
Approach to Sustainable, Greener Cleanup
Pharmacia & Upjohn Company LLC Site Site Background and Selected Remedy
CMI Greener Cleanup Design/Execution and Best Management Practices (BMPs)
Project Recognition – Greener Cleanup

## Slide 3: Why Sustainable, Greener Cleanup?
Pfizer’s core value of “Respect for Society”
  Communities want properties returned to beneficial use
  Experience has shown that, given the option, communities are receptive to safe and sustainable solutions
Value Proposition:
  Reduce environmental footprint
  Increase social responsibility and community acceptance
  Obtain regulatory acceptance
  Reduce remedial construction and long-term costs
  Gain economic benefit to the community
  Achieve cleanup!

## Slide 4: Some General Principles
Start with Conceptual Site Model and plan with end in mind
Identify and engage appropriate stakeholders early in the process
Consider environmental footprint and greener cleanup design through-out life cycle of investigation, remedy, and OM&M
To the extent possible, preserve and enhance the assets of the property and create opportunities for beneficial reuse
Seek opportunities to incorporate green remediation techniques in the design and implementation phase
Where appropriate, ensure future use is consistent with the site’s location in the community and in the environment

## Slide 5: Pharmacia & Upjohn Company LLC Site North Haven, CT
Site Background &
Selected Remedy
Case Study

## Slide 6: Pharmacia & Upjohn Company LLC Site
1800s - 1944
1948 - 1996
1998 - Present
Circa 2003
Notes: How Pfizer became responsible for The Upjohn Company site.

## Slide 7: Site Conditions – Post Operations
Primary Causes
  140 year industrial history
  Releases from aboveground / underground tank operations
  Use of lagoons (former clay borrow pits) for wastewater treatment
  Onsite stockpiling of wastewater treatment residuals/sludge
Resulting Site Conditions
  Chemical impacts in soil, groundwater and adjacent title flat sediments
  Constituents include broad range VOCs, SVOCs, PCB and metals
  Areas with free phase organics (DNAPL) below water table
  Large quantities of impacted waste water residuals/sludge
  Shallow groundwater impacts across the Site
  Limited impacts below aquitard
Regulatory Drivers
  RCRA 3008(h) Corrective Action Order
  CT Transfer Act

## Slide 8
Greener Cleanup Design/Construction Considerations
Environmental footprint
Overall chemical mass removal (i.e. DNAPL area)
Impact/nuisances to the community
Remediation worker safety
Beneficial reuse of Site
Public support for remedy
Short term vs long term costs
Core elements for greener cleanup (defined by ASTM)
  Energy
  Air
  Water
  Land & Ecosystems
  Materials & Waste

## Slide 9: CMS Carbon Footprint Comparison Energy, Air, Water, Materials & Waste, Land Reuse
Chart: 
| Long-Term O&M | Caps and Covers | ISTT | Soil & GW Treatment | CMA #2 | CMA #3 | CMA #4 | CMA #5
Mass of CO2 Emissions (tons) | 26790 | 24428 | 28933 | 38918

## Slide 10
Key Components of EPA Approved Remedy
  Groundwater control and treatment, long-term operations
  East Side Components
  Sediment removals, tidal wetlands mitigation
  Eastern side consolidation, protective barriers, ecological enhancements
  West Side Components
  Thermal desorption to treat the most impacted area
  Western side protective barrier
Notes: The bullet in red will be discussed in this presentation.

## Slide 11: Key Components of CMS Selected Remedy
Hydraulic Containment with Barrier Wall and GW Treatment
In-Situ Thermal
Consolidation and Capping
Constructed Wetlands

## Slide 12: Sediment Removals Land & Ecosystems: Conserve, Protect & Restore
Sediment Removals
2013 - 2014
Tidal Wetland Mitigation
2014 - 2015

## Slide 13: Groundwater Control Water: Improve Quality, Decrease Quantity of Use
Initial upgrades to existing Groundwater Treatment Facility
  2012 - 2013
Installation of Perimeter Hydraulic Barrier Wall
  2013
Expansion of Groundwater Extraction System
    2013 - 2014
Final retrofit of existing GWT Facility
    On-Going

## Slide 14: In-Situ Thermal Remediation of DNAPL Energy: Reduction, Efficiency and Renewables
Full-scale & Pilot-scale design, construction, operation, decommissioning
    2014 – 2016
    275,000 lbs removed
      Dichlorobenzenes
      PCBs

## Slide 15: East Side Consolidation, Stabilization, Covers Materials & Waste: Minimize, Reuse, Recycle
  Reuse of onsite soil for grading below caps thus reducing volume of imported fill material
    2013
    New cover system completed including final cover and planting
      2014
North Pile

## Slide 16: East Side Ecological Restoration Land & Ecosystems: Conserve, Protect & Restore
Ecological restoration and Tidal Wetland Mitigation
  Creation of 6+ acres of new freshwater wetland habitat
Planting and subsequent monitoring / maintenance
2014 – On-going

## Slide 17: Pharmacia & Upjohn Company LLC Site North Haven, CT
CMI Sustainability and Greener Cleanup BMPs
Case Study

## Slide 18: Greener Cleanup Value-Added: Not Just Money Saved
  The cost of Greener Cleanup is not only measured in dollars but also the comparative environmental footprint over the project life-cycle as well as the timeframe for return of the property to future beneficial reuse
  The currency of added value or reduced costs must be viewed in terms of resources consumed and impacts to the environment, as well as dollars spent

## Slide 19: Notable Green BMPs
Identified over 75 Green BMPs
Key environmental BMPs include:
  Consolidation of over 80,000 cubic yards of “cut” material and drill cuttings under engineered caps, avoiding off-site disposal and importing fill
  Reduction of groundwater extraction rates by 50% via use of subsurface cutoff wall and covers
  Creation of 6+ acres of fresh water and tidal wetlands mitigation
  Use of approximately 2,500 tons of blast furnace slag, a manufacturing byproduct, in hydraulic barrier wall construction
  Use local labor, suppliers and labs when possible to reduce daily transportation
Key economic BMP
  Local buying commitment
        North Haven - 7% of project purchases to date
        Within 25 miles – 44% of project purchases to date
        State of CT – 58% of project purchases to date

## Slide 20: Review of Green Remediation Cost Impacts for North Haven
Green Remediation Aspects | Cost Impacts
Use of local labor resources (where feasible) | Cost neutral since this was included in contract terms at the beginning of the contract
Use of recycled material in hydraulic barrier wall mix design | Unit cost comparable to other reagents – Change in mix design resulted in project cost change
Hydraulic barrier wall at toe of slope | Resulted in reduction of HBW mix and elimination of a MSE wall
Low permeability cover system with storm water directed to BMP/wetland restoration area | Results in 50% reduction in groundwater treatment flows due to reduced storm water infiltration (treatment plant operational savings)
In-Situ Thermal Remediation (ISTR) | ISTR costs offset by cost avoidance (savings) for need of DNAPL waste incineration at Port Arthur, TX
Consolidation of on-site material for cover system sub-grade | Reduced amount of clean fill import that was needed by 80,000 cu yds

## Slide 21
60 acre ecological restoration
Re-established lost habitat
Creation of on-site wetlands
Selected re-vegetation requires minimal mowing
Controlled public access
17-acres designated for economic development
On-going
Sustainability in Reuse Plan
Land & Ecosystems: Conserve, Protect & Restore

## Slide 22: Pharmacia & Upjohn Company LLC Site North Haven, CT
Project Recognition
Greener Cleanup
Case Study

## Slide 23
EPA Recognition of Achievements

## Slide 24
CT DEEP Green Circle Sustainability Award
  Project recognized for its sustainability and green remediation initiatives
    One of 59 final nominees
    One of 15 award winners
    One of 4 businesses recognized
  Project recognized for its sustainability and green remediation initiatives
  Green Circle award presented by CT DEEP Commissioner and USEPA Regional 1 Administrator
Notes: The bullet in red will be discussed in this presentation.