## Slide 1: DISCLAIMER Notice: This presentation has been provided as part of a U.S. Environmental Protection Agency webinar. The document does not constitute EPA policy. Mention of trade names or commercial products does not constitute endorsement or recommendation for use. Links to non-EPA web sites do not imply any official EPA endorsement of or a responsibility for the opinions, ideas, data, or products presented at those locations or guarantee the validity of the information provided. Links to non-EPA servers are provided solely as a pointer to information that might be useful to EPA staff and the public.

## Slide 2
How to make RCRA hazardous waste regulations & policies work for you in cleaning up a site.
By: Cheryl Nelson USEPA Region 9, San Francisco
Think before you dig!
Notes: This webinar will introduce some of the flexible RCRA policies and regulations, that can assist in removing barriers to full and effective clean up of contaminated sites.
These flexible policies and regulations apply to any contaminated site clean up that has potentially RCRA hazardous media (such as contaminated soil, sediment, surface or groundwater) or other hazardous waste or debris (such as building materials).
The most important things to take away from this webinar:
Think it through before you dig. Digging contaminated soil/debris often triggers (unnecessarily) cumbersome RCRA regulations (such as the Land Disposal Restriction Treatment Standards (LDRs)) that can be avoided or minimized with advance planning.
Identify the best site remedy based upon future land use and mitigating site risk.
Prepare an accurate waste identification under RCRA for all potentially contaminated materials at the site.
Work backwards from the remedy to find the best flexible policy/pathway to get there.
Use the Contained-in-Policy and the Area of Contamination Policy to help avoid triggering the LDR’s unnecessarily.
Use the alternative LDR treatment standards for contaminated soil (40 CFR 268.49), and the treatment standards for hazardous debris (40 CFR 268.45) to significantly reduce the need to treat these materials when LDR’s can’t be avoided. Use the Variance from a Treatment Standard (40 CFR 268.44) to significantly reduce (or eliminate) the need to treat these materials if LDR’s can’t be practically met.
Use the generator treatment or other RCRA recycling or treatment exclusions to avoid having to get a RCRA permit.
Document all of your decisions/policies in your public documents and statement of basis.
THINK BEFORE YOU DIG!!

## Slide 3: Why is this topic important?
There is a large universe of contaminated sites waiting clean up
EPA wants to encourage clean up and re-use of contaminated sites
There is a common misperception that RCRA regulations prevent cost-effective clean up
There are many RCRA policies/regulations that remove barriers to aggressive/effective clean up
These policies/regulations mostly only work if you invoke/plan for them BEFORE you start digging.
Notes: Throughout my career both in private practice and at EPA as a RCRA expert, I have been consulted on cleanup projects. The first question I always get asked is either: “Every hazardous waste landfill has rejected our waste, what do we do now?” or “What remedy can I choose that avoids RCRA regulations or having to dispose all the waste at a hazardous waste landfill”?
I always advise that these are backwards ways to think about and approach a site clean up. The right way to think about a site clean up is to begin with the end in mind.
In reality there are many flexible RCRA policies/regulations that remove barriers to aggressive/effective clean up and allow for timely, implementable solutions. However, you need to do careful planning ahead of time to invoke/use these policies/regulations.
Too many people rush to just “get the stuff out of here” and end up either out of compliance with RCRA and/or generating a huge amount of stuff (debris, soil, carbon, water, etc.) that then has to be disposed as hazardous waste. In extreme cases the clean up can also trigger the need for a RCRA HW permit, long term O& M and/or costly treatment, disposal, or incineration.

## Slide 4: Bottom Line:
Think it through before you dig!
Notes: It has been my experience that the overall cost of a clean up is often dictated by the volume of RCRA hazardous waste that is generated/treated/disposed even if that volume is small compared to the volume of other non-hazardous wastes generated at a site.
So its worth thinking through ahead of time your overall plan for clean up (consistent with your site-specific cleanup objectives) to ensure that you don’t unnecessarily generate hazardous waste if you don’t have to!

## Slide 5: The Successful Cleanup Process
Choose your cleanup remedy. (This is generally based upon the site-specific risk and future land use but also includes other factors (e.g. post-construction controls, community acceptance, cost, etc.)
Make a waste determination for all waste streams; determine which are hazardous
Determine if LDR treatment standards apply (attach) to each hazardous waste stream, and where in the cleanup process (i.e., where is the point of generation?)
If LDRs attach, choose which treatment standards apply (e.g. UHCs; alternative soil standards, etc.)
Work backwards from the chosen remedy to pick the most flexible RCRA regulatory unit/policy/tool that will achieve both the risk numbers (cleanup goals) and, where applicable, LDR treatment standards.
Notes: The successful cleanup process begins with the end in mind!

## Slide 6: 7 Keys to Successful clean up
Identify the optimum site remedy based upon future land use and mitigating site risk.
Prepare an accurate waste identification under RCRA for all potentially contaminated materials at the site. (This can be done by developing and using a conceptual site model to guide site characterization and identification of wastes).
Work backwards from the remedy to find the best RCRA flexible policy/pathway to get there.
Use the Contained-in-Policy and the Area of Contamination Policy to help avoid triggering the LDR’s unnecessarily.
Notes: I’ve learned in my RCRA career of working on cleanup sites that there is an order/hierarchy in which to approach a site clean up that works the most successfully.
The 7 Keys to Success are the take away message from this webinar. In the next several slides I’ll go into more detail on each of these steps and give you my “go to” resources for how to accomplish these.

## Slide 7: 7 Keys to Successful clean up (Continued)
Use the alternative LDR treatment standards for contaminated soil (40 CFR 268.49), and the treatment standards for hazardous debris (40 CFR 268.45) to significantly reduce the need to treat these materials when LDR’s can’t be avoided. Use a site-specific variance from a treatment standard (40 CFR 268.44 (h)) if it is unachievable to meet the LDR’s or if it is inappropriate to do so.
Use the generator treatment or other RCRA recycling or treatment exclusions to avoid having to get a RCRA permit.
Document all of your decisions/policies in your public documents and statement of basis.
Notes: I’ve learned in my RCRA career of working on cleanup sites that there is an order/hierarchy in which to approach a site clean up that works the most successfully.
The 7 Keys to success are the take away message from this webinar. In the next several slides I’ll go into more detail on each of these steps and give you my “go to” resources for how to accomplish these.

## Slide 8: First Key to Success/Resources
Identify the optimum site remedy based upon future land use and mitigating site risk.
Presumptive Remedies
http://www.epa.gov/superfund/policy/remedy/presump/pol.htm
Handbook of GW Protection and cleanup Policies for RCRA Corrective Action
http://www.epa.gov/wastes/hazard/correctiveaction/resources/guidance/gw/gwhandbk/index.htm
RCRA Subpart S Corrective Action Guidance
http://www.gpo.gov/fdsys/pkg/FR-1996-05-01/pdf/96-9707.pdf
Notes: When choosing a site remedy, you should primarily base your initial decision upon risk management and future land use. There are enough flexible RCRA policies to remove costly barriers to implementing the chosen remedy such that “avoidance” of RCRA regulation shouldn’t be a significant factor in your remedy decision.

## Slide 9: Second Key to Success/Resources
Prepare an accurate waste identification under RCRA for all potentially contaminated materials at the site. (This can be done by developing and using a conceptual site model to guide site characterization and identification of wastes).
Definition of Solid Waste webpage (includes DSW tool and links to key regulations)
http://www.epa.gov/epawaste/hazard/dsw/index.htm
Contained in Policy
http://www.epa.gov/epawaste/inforesources/online/index.htm
RCRA Online (EPA database of key policies/letters)
http://www.epa.gov/epawaste/inforesources/online/index.htm
Site Conceptual Model
http://www.epa.gov/osw/hazard/correctiveaction/pdfs/workshop/csm_slides.pdf
Notes: To prepare an accurate waste identification do the following:
Make a list of ALL the possible/probable wastes from a site clean up. Don’t forget to include things like contaminated soil, groundwater, spent carbon, PPE, building debris, etc.
For EACH of these wastes do a SEPARATE initial (before sampling/analysis/removal) waste identification documenting your logic and possible outcomes.
For potentially hazardous wastes that might have a significant impact on the project cost and/or proposed remedy decide if sampling/testing are advised/necessary and WHICH tests to perform. Be aware that the types of sampling/tests that landfills might require for disposal are DIFFERENT than the types of sampling/tests that you will need to determine IF the waste is hazardous. Do a quick cost/benefit analysis to determine whether to DO the sampling/testing and/or just ASSUME that the waste is hazardous. Be sure to include in your analysis the cost of LDR treatment and waste disposal.
For contaminated media (soil/groundwater) - consult the Contained In Policy and make an initial determination if the media as it exists prior to digging it up “contains” listed hazardous waste. If you can, document (in writing in your record of decision) that the media does NOT contain listed hazardous waste after considering the source of the contaminant and WHEN the media was contaminated relative to the listing date (e.g. a spill that occurred PRIOR to the listing date of that listed hw is NOT considered a hw IF you make the contained in decision BEFORE you dig it up).
Conduct any sampling/testing for determining waste identification. Update all waste identifications with info from steps 4 and 5.

## Slide 10: Tips for identifying contaminated media
Environmental media (soil, groundwater, sediment) are not “solid wastes” under RCRA and hence cannot be hazardous wastes if contaminated.
However, under EPA’s Contained in Policy, contaminated environmental media can become subject to regulation under RCRA if they “contain” hazardous waste such as when:
a) they exhibit a characteristic of hazardous waste or
b) when they are contaminated with concentrations of hazardous constituents from listed hazardous wastes that are above health-based levels

## Slide 11: Tips for determining Listed Hazardous Wastes
Understand the relationship between when a chemical was spilled, versus the effective date of when it was listed as a hazardous waste (e.g. when it was/becomes subject to RCRA).
Listed wastes created, spilled, or disposed prior to their respective listing date haven’t been “generated” yet and therefore aren’t hazardous wastes
  when subsequently disturbed, excavated, or managed then they are “generated” and then are hazardous wastes
Listed wastes created, spilled, or disposed after their respective listing date have already been “generated” and are already listed hazardous wastes.
Notes: Remember: Don’t ASSUME you have a listed waste unless you KNOW that you have one. However, you MUST do a “reasonable” amount of research to look for documentation/evidence that a listed waste was used/generated at a particular site and when it might have been spilled/disposed.

## Slide 12: Point of generation for media contaminated with listed hazardous waste
Notes: Three principles informed EPA’s policies on application of LDRs to contaminated media.
First-All hazardous waste are prohibited from land disposal (40 CFR 268 Subpart C) unless/until they meet their applicable LDR treatment standards.
Second-once a decision has been made to “generate” and land-dispose contaminated environmental media, LDRs generally apply only to contaminated environmental media that contain hazardous waste or that exhibit a hazardous characteristic. Exception to this rule flows from principle three.
Third-once LDRs attach to any given hazardous waste (including hazardous waste contained in environmental media or media that exhibit a hazardous characteristic) the LDR treatment standards continue to apply until they are satisfied. Elimination of the “hazardousness” of the waste or contaminated environmental media does not automatically satisfy LDRs.

## Slide 13: Third Key to Success/Resources
Work backwards from the remedy to find the best RCRA flexible policy/pathway to get there.
History of RCRA Corrective action
http://www.epa.gov/epawaste/hazard/correctiveaction/resources/guidance/gen_ca/cafs1.pdf
Management of Remediation Waste Under RCRA
http://yosemite.epa.gov/osw/rcra.nsf/0c994248c239947e85256d090071175f/D9E61A0505DB4B6885256817006E32B8/$file/14291.pdf
Notes: Work backwards from your chosen remedy to your starting point to determine the various interim steps needed to implement the remedy.
At each interim step plan out (before you dig) all of the activities associated with each separate potentially hazardous waste stream.
At each activity evaluate whether this activity will cause the waste to become hazardous (e.g. you will be “generating” it and thereby triggering the need to meet the generator requirements for proper storage), and/or whether the activity will trigger the need for a permit for storage/treatment.

## Slide 14: Fourth Key to Success/Resources
Use the Contained-in-Policy and the Area of Contamination Policy to help avoid generating waste and/or triggering the LDR’s unnecessarily.
Contained in policy
http://yosemite.epa.gov/osw/rcra.nsf/0c994248c239947e85256d090071175f/1709125b14c9f0548525670f006bf311!OpenDocument
Use of the Area of Contamination (AOC) Concept During RCRA Cleanups
http://yosemite.epa.gov/osw/rcra.nsf/0c994248c239947e85256d090071175f/E6CAC7C42B27CE048525670F006BF350/$file/11954.pdf
Compilation of guidance on remediation waste policies
http://www.epa.gov/epawaste/hazard/correctiveaction/resources/guidance/index.htm
Notes: There are two very useful RCRA policies that can help avoid generating waste and/or triggering LDR’s once generated: the Contained in Policy, and the Area of Contamination Policy.
Because these are policies they don’t appear in regulation. However, States that are authorized for the RCRA program can have regulations that are broader in scope or more stringent than EPA, so consult with the approved State program before invoking these policies.
The Contained in Policy applies to any potentially hazardous media and helps clarify when that media “contains” listed hazardous waste and must therefore be managed as hazardous or when that media “no longer contains” listed hazardous waste (generally when concentrations of the listed constituents are below health-based limits and the media does not exhibit a characteristic). This policy is most useful in situations where soil/gw has become contaminated with a listed hazardous waste in diminimus or small quantities. The “key” is to apply the policy BEFORE you generate the waste and thus avoid RCRA altogether. The act of “generating” the waste triggers the LDR’s which MUST be satisfied even if that means treating the waste below the concentrations that would otherwise make the waste hazardous.
If you invoke the Contained in Policy be sure to document your analyses in the record of decision or other statement of basis BEFORE you dig up/move any wastes.
Note that for debris that contains a listed hazardous waste there is a provision (40 CFR 261.3(f)) that works similarly to the contained in policy for media. That provision allows debris that has been treated using one of the required extraction or destruction technologies and/or for which the Regional Administrator makes a determination that the debris is no longer hazardous to exit RCRA C regulation.
The Area of Contamination Policy generally allows consolidation and in-situ treatment within a discrete area of dispersed contamination without triggering “generation” of the waste and therefore without triggering LDRs. The key is that treatment is only allow in-situ (e.g. you can’t containerize it or move it to another location. This policy is very useful for consolidating contaminated materials into a smaller footprint and/or treating in place.

## Slide 15: Fifth Key to Success/Resources
Use the alternative LDR treatment standards for contaminated soil (40 CFR 268.49), and the treatment standards for hazardous debris (40 CFR 268.45) to significantly reduce the need to treat these materials when LDR’s can’t be avoided.
Use a site-specific variance from a treatment standard (40 CFR 268.44 (h)) if it is unachievable to meet the LDR’s or if it is inappropriate to do so.
40 CFR 268.49, 40 CFR 268.45, 40 CFR 268.44
  http://www.gpo.gov/fdsys/pkg/CFR-2014-title40-vol27/pdf/CFR-2014-title40-vol27-part268.pdf
LDR Phase IV Preamble on contaminated soil (63FR 28602)
  http://www.gpo.gov/fdsys/pkg/FR-1998-05-26/pdf/98-12575.pdf
Superfund Guidance on LDR variances:
  http://www.epa.gov/superfund/policy/remedy/sfremedy/arars/rcra.htm
Notes: If you have contaminated soil that is hazardous and can’t avoid “generating” the waste and/or “triggering” the LDR standards then the next thing to do is to look at the alternative LDR standards for contaminated soil.
The alternative LDR standard for contaminated soil is much more “generous” (e.g. easier to meet) than the regular LDR standard, and in a majority of cases might not require any treatment at all if the contaminated soil “as is” is below this standard!
The alternative soil LDR is 90% reduction in concentration of contaminant (based on total concentrations for most non-metals and soluble concentrations for metals) capped by (no lower than) 10 times the Universal Treatment standard for that contaminant AND for contaminated soil that exhibits a characteristic of ignitability, corrosivity, or reactivity, the soil must be treated to eliminate the characteristic.
This standard applies to not only the main contaminants that make the soil “hazardous” but also to any underlying constituents that have an initial concentration above 10 times the UTS.
If you STILL cannot meet an applicable treatment standard either physically or practically (e.g. too expensive, would discourage aggressive removal, would require incineration of soil, etc.) you can seek/approve a site-specific variance from a treatment standard. An alternative standard could be set such that the concentration of the contaminated material “as is” is below the alternative standard rendering treatment moot. (See superfund guidance that describes how to apply/document for the variance and various justifications that can be used to support it.)
If you have contaminated debris that is hazardous then you must weigh the cost/benefit of either treating (to meet the alternative treatment standards in 40 CFR 268.44) the debris onsite to render it non-hazardous and exiting RCRA C control or just managing the debris as hazardous under RCRA C. In the latter case you must also weigh the cost/benefit of treating to meet LDR’s onsite or offsite.
Note that the alternative treatment standards for debris are technology and performance based and vary depending upon the physical nature of the debris and the chemical nature of the contaminant.
If the hazardous debris is contaminated with a listed hazardous waste, then treating via one of the extraction or destruction technologies will render the debris non-hazardous and remove RCRA C control (40 CFR 261.3(f)).

## Slide 16: Sixth Key to Success/Resources
Use the generator treatment or other RCRA recycling or treatment exclusions to avoid having to get a RCRA permit.
Generator Treatment
  http://yosemite.epa.gov/osw/rcra.nsf/0c994248c239947e85256d090071175f/57ac820a47a8bc4e85256d1600748c43!OpenDocument
Management of Remediation Waste Under RCRA
  http://yosemite.epa.gov/osw/rcra.nsf/0c994248c239947e85256d090071175f/D9E61A0505DB4B6885256817006E32B8/$file/14291.pdf
Notes: If you can’t avoid triggering treatment standards and it’s cost effective to treat hazardous wastes onsite, then think carefully about what type of treatment “unit” will be needed. There are several options available that would not require a full hazardous waste permit. These options are much more practical/cost effective than trying to get a new hazardous waste permit or having to modify an existing permit at the site for a new unit.
Area of Contamination Policy- Allows treatment in situ without triggering LDRs or Minimum technology standards and without a permit. Key is in situ (can’t dig it up/containerize it) and can’t move it to a uncontaminated area. But can push it around/consolidate it.
“Generator treatment” exclusion- Basically if the treatment can be done in a tank or container within the 90 day “clock” and conforms to all the generator tank/container storage requirements (e.g. doesn’t involve any application of heat) then you don’t need a permit.
Take a close look at the exclusions in 40 CFR 261.4 and at the permit exemptions in 40 CFR 270.1 (c)(2) to see if any of these offer relief for your specific situation.
Consider using a “CAMU”, “Temporary Unit” or “Staging Pile” (40 CFR 264 Subpart S)- These units can be invoked by EPA/State in an “enforceable document” such as order and don’t require a full permit. Some minimum technology requirements and storage limitations apply.
Emergency removals, CERCLA response actions, and immediate responses to spills generally don’t require a permit.
If you must get a permit then consider Permits by Rule, Emergency permits, Standardized Permits, or Remedial Action Plans (40 CFR 270 Subpart F) as these aren’t as onerous to obtain as a full RCRA permit.

## Slide 17: Seventh Key to Success/Resources
Document all of your decisions/policies in your public documents and statement of basis.
Statement of Basis
http://www.epa.gov/epawaste/hazard/correctiveaction/sbs2/index.htm
Risk-based clean closure guidance
http://www.epa.gov/epawaste/hazard/correctiveaction/resources/guidance/risk/cclosfnl.pdf
Notes: No matter how you end up at your final remedy it’s imperative that you document all of your thinking/decisions in the record that will be available for public review/comment. This is especially true even if your remedy is an interim or partial remedy that you haven’t yet sought public comment on.

## Slide 18: Other Resources
Corrective Action Main Webpage:
http://www.epa.gov/epawaste/hazard/correctiveaction/resources/guidance/index.htm
RCRA Information Network (RIN) Call
  A national monthly call (first Wednesday of the month at 2 pm EDT) of EPA and State Staff to discuss a wide range of issues related to regulatory interpretation of the RCRA program. Hosted by EPA HQ office: ORCR (Jim O’Leary)
Webpage on use of RCRA ARARS at Superfund sites:
http://www.epa.gov/superfund/policy/remedy/sfremedy/arars/rcra.htm
RCRA Corrective Action Enforcement Authorities
http://www2.epa.gov/enforcement/rcra-corrective-action-enforcement-authorities

## Slide 19: Case Study/Example
You are the lead regulator for a site that formerly operated a vapor degreaser from 1980 to 1992 that resulted in Tetrachloroethylene (PCE) contamination of soil beneath the building that held the degreaser.
Concentrations of PCE in soil range from ND up to 450 ppm. The owner’s proposed remedy is to demolish the degreaser/building, and excavate contaminated soil above the cleanup level (5 ppm) and dispose all to a local Subtitle D landfill. Is this acceptable?
What are the potential waste streams for this site? Are any hazardous?
Are any of the wastes subject to LDRs?
What do you think of the owner’s proposed remedy? What additional requirements, if any, would you impose?
What other options does the owner have to avoid triggering costly RCRA regulations?

## Slide 20: Case Study Solution
The potential waste streams are:
Contaminated soil with PCE a listed waste F001 (spilled after effective date of regulation see 40 CFR 268 Appx. VII); need additional data (TCLP test) to determine if also D039
Degreaser/building debris contaminated with PCE with a listed waste F001; also potentially D039
Media and Debris contaminated with a listed waste are subject to the contained-in-policy. Refer to table VII in 40 CFR 261 for the list of constituents for which each listed waste is listed for. For F001 constituents include:
Tetrachloroethylene, methylene, chloride, trichloroethylene, 1,1,1-trichloroethane, carbon tetrachloride, chlorinated fluorocarbons
To make a contained in determination, would need additional data such as soil concentrations of the above constituents. Also need sampling/analytical data from the degreaser and building debris for all these constituents.
To make the contained in decision, need to compare the concentrations of chemical constituents against health-based risk concentrations.

## Slide 21: Case Study Solution
Do LDR’s apply?
The site operated from 1980 to 1992 and therefore chemicals were spilled both prior to and after the effective date of listing (1986 according to Table 1 in Appendix VII in 40 CFR 268). The wastes therefore were subject to LDRs when spilled after 1986. LDRs therefore, attached when the spill occurred and now must be satisfied.
For the soil: can either meet the numeric standards for F001 in 40 CFR 268.40 or the alternative soil treatment standard of 90% reduction or 10X UTS in 40 CFR 268.49.
For the debris: can either meet the numeric standards for F001 in 40 CFR 268.40 or the alternative debris standards in 40 CFR 268.45

## Slide 22: Case Study Solution
Is the proposed remedy acceptable?
The contaminated soil and potentially contaminated debris are both listed hazardous wastes and subject to LDRs. Therefore, without treatment and a contained in decision, the soil and debris cannot be disposed in a local (subtitle D) landfill, but must be managed and disposed as listed hazardous waste.
Additional requirements that should be imposed are:
Owner is subject to RCRA generator regulations (must have an ID #, must manage/store the waste as hazardous (e.g. drummed, labeled, less than 90 day accumulation), waste must be manifested to a permitted TSDF.

## Slide 23: Case Study Solution
Other Options:
Segregate soil during excavation to minimize amount that must be disposed as hazardous. Treat soil to meet LDRs, and if this is below risk-based levels then contain out/dispose to Subtitle D landfill.
Consolidate soil inside Area of Contamination and use generator treatment in tanks/containers to meet LDRs. And/or petition for LDR variance if the LDR’s are inhibiting aggressive remediation or are not achievable.
Treat debris using destruction/removal standard; then contain out/dispose to Subtitle D landfill. Or, metal can be decontaminated and reclaimed as scrap and/or reused.
Consolidate soil in Area of Contamination and treat in-situ to meet LDRs and then cap. If capping not protective or if area of contamination is not contiguous then build a CAMU. CAMU would require a RCRA permit, RAP, or Order.

## Slide 24: Lesson Learned! Think it through before you dig
In some cases digging up contaminated soil “generates” the soil to become a RCRA hazardous waste!
Once “generated” you can’t “un-generate” it.
If the soil/waste is subject to the Land Disposal Restriction Standards then you have also “triggered” the need to treat the soil/waste.
Some treatment standards require incineration (!) adding exponentially to the cost of the clean up.
Even without treatment the cost of hauling and disposing the soil/waste will significantly add to your site clean up.
Notes: One of the biggest “lessons learned” in dealing with RCRA and site cleanups is to think it through before you dig.
Here’s why….

## Slide 25: Lesson Learned! (Continued) Think it through before you dig
Once “generated” a 90-day clock starts ticking that requires you to remove the soil/waste from the site and treat/dispose it at a RCRA HW facility.
If you run out the 90-day clock then you “trigger” the need for a RCRA permit for storage at the site. This will exponentially add to the time and cost for the clean up.
You can often avoid ALL of these “triggers” if you think it through and plan for it before you dig it up!
Notes: One of the biggest “lessons learned” in dealing with RCRA and site cleanups is to think it through before you dig.
Here’s why….

## Slide 26: Important Take Home Messages
Decide what the “right thing” to do is for the clean up given the future use of the property
Work backwards from this outcome to ensure that all aspects of the clean up are planned before proceeding
Identify if you have any hazardous waste or hazardous contaminated media or debris (where and how much)
Use the RCRA flexible policies and regs to avoid triggering unnecessary RCRA regulation/disposal and reduce cost
THINK BEFORE YOU DIG!!