## Slide 1
Evaluating and Controlling Mercury in Aquatic Ecosystems
Moving Beyond Source Control
September 25th, 2013
Stephen Dent, PhD
Environmental Engineer
EPA Region 9 Hg Workshop

## Slide 2: Presentation Objectives
Introduce Mercury Issues
  Relation to Eutrophication/Anoxia
Lake Management – Controlling Anoxia
  Oxygenation Systems
  Twin Lakes Study
  Other Applications
Concluding Thoughts/Management Considerations
Questions
Overview
CH3Hg+

## Slide 3
Scope of Mercury Issues in US
Importance
367 Stream Sites Sampled Across United States
Sites with Fish Greater than 0.3 ug/g
  25%
Sites with Fish Greater than 0.6 ug/g
  10%

## Slide 4: Conceptual Hg Model
Hg Dynamics

## Slide 5: Oxygenation Systems
DIFFUSER PIPE
Beutel, M.W. and A.J. Horne. 1999. A review of the effects of hypolimnetic oxygenation on lake and reservoir water quality. Lake and Reservoir Management. 15(4):285-297.
Lakes

## Slide 6: Linear Diffuser System
Lakes

## Slide 7: Twin Lakes, WA
Lakes

## Slide 8: Hypothesis
The working hypothesis for this component is that the maintenance of an oxygenated sediment/water interface and hypolimnion will reduce the Fe, Mn, and MeHg concentrations within the water column and in biota.
Lakes

## Slide 9: Results – South Twin
Lakes
mg/L
µg/L
µg/L
ng/L

## Slide 10
Lakes
Results – North Twin
mg/L
µg/L
µg/L
ng/L

## Slide 11
Results - Profiles
Lower Hypolimnion: 50 to 75% Reduction.
Upper Hypolimnion: 50 to 90% Increase.
NT
ST

## Slide 12: 2009 and 2010 Mercury in Zooplankton
Chart: 
| 6/30/2009 | 7/23/2009 | 8/13/2009 | 9/3/2009 | 9/24/2009 | 10/13/2009 | 10/29/2009 | 11/13/2009 | 4/22/2010 | 5/7/2010 | 5/19/2010 | 6/9/2010 | 6/29/2010 | 7/28/2010 | 8/27/2010 | 9/24/2010 | 10/8/2010 | 11/12/2010
North Twin | 63.5124 | 105.4069 | 102.2239 | 127.3916 | 103.3945 | 117.2326 | 46.7432 | 0 | 73.0327 | 61.9652 | 84.3892 | 118.3195 | 148.6232 | 179.8125 | 168.6027 | 282.2553 | 188.0468 | 127.281
South Twin | 41.9408 | 59.4568 | 97.5108 | 113.8844 | 58.027 | 49.232 | 67.5442 | 79.377 | 47.7567 | 90.626 | 27.2435 | 56.4608 | 93.7557 | 101.2887 | 35.2563 | 58.5481 | 62.5761 | 51.0331

## Slide 13: Sediment Sensitivity
Bryant, L, Gantzer, P., Little, J. 2011. Increased sediment oxygen uptake caused by oxygenation-induced hypolimnetic mixing. Water Research. 45, 3692-3703.
Small Variations in Oxygen in Bulk Water Column.
Large Oxygen Deficit at Sediment Water Interface

## Slide 14: Measurement Limitations- DO vs Fe and Mn in NT
Lakes

## Slide 15
Surrogate Redox Parameters – MeHg Covariance with Fe and Mn in NT
Lakes

## Slide 16: Summary
Oxic Sediment Water Interface Not Maintained at NT
  Horizontal Oxygen Delivery Location
Negative Feedback: Metals Release W/ Mixing
  Release of Fe, Mn, and Hg,
Sampling Plan Design Critical For Tracking Performance
  Parameters
    The Hg Cycle is Tightly Linked to Fe and Mn Cycles
    Redox
  Spatial/Temporal Sampling Regime
Lakes

## Slide 17: Concluding Thoughts
Hypolimnetic Oxygenation Can be Used to Control Mercury Accumulation in Lakes and Reservoirs,
  Very sensitive to how the system is designed and managed.
Data Gaps with Existing In Situ Eutrophication Strategies in Relation to Hg.
  Hypolimnetic Oxygenation,
  Nitrogen Addition,
  In Situ Treatments.

## Slide 18: Special Thanks To:
Washington State University
  Dr. Marc Beutel
  Dr. Dave Yonge
  Dr. Rick Watts
  Dr. Barry Moore
  Dr. Doug Call
  The Countless Graduate Students from CEE and NATRS
  Colville Confederated Tribe
    Dr. Ed Shallenberger
Battelle Marine Science Laboratory
  Dr. Gary Gill
  Brenda Lasorsa
Agouron Institute
National Science Foundation’s GK-12 Program
WSU’s Culturally Relevant Engineering Applications in Mathematics (CREAM)

## Slide 19: Questions?

## Slide 20: Results-Oxygen Addition
2009: 30 SCFM
  Lease hypolimnetic metals input.
2010: 40 SCFM
  Most hypolimnetic metals input.
2011: 35 SCFM
  In between.
Chart: 2010
| May | June | July | Aug. | Sept. | Oct.
ave Ox Addition | 28.4667 | 26.0333 | 36 | 40.4839 | 40.0333 | 34.7857
DO ave | 7.6775 | 6.2549 | 6.1337 | 6.3066 | 5.3611 | 7.0222
Chart: 2011
| May | June | July | Aug. | Sept. | Oct.
Ave Ox Addition | 37.2333 | 39.9032 | 34.5484 | 39.7 | 32.8
DO ave | 5.4791 | 6.8767 | 7.9065 | 7.7295 | 7.0454 | 8.0368
Chart: 2009
| May | June | July | Aug. | Sept. | Oct.
ave Ox Addition | 35 | 35 | 31.129 | 25 | 28.7333 | 33.25
DO ave | 8.5646 | 10.6428 | 11.8624 | 9.542 | 8.4075 | 8.8651

## Slide 21: Factors Correlating with Fish Tissue (LMB) in Streams
Land Use Influences
  Hg in Tissue Correlates with % of Undeveloped Watershed
Land Cover influences
  Bioaccumulation Correlated with Basin % of Forest and Woody Wetland
Chemical Influences (A More Precarious Link)
  Unfiltered MeHg
  Sediment MeHg Normalized to OM (Related Back to Land Cover)
  Low pH
  Dissolved Sulfate
Rivers and Streams

## Slide 22: Anthropogenic Point Source Impacts
Minamata Bay
Importance
Acetaldehyde Production 1932 -1968
27 Tons Methylmercury Dumped Into the Bay
First Case: 1956
900 Killed
2 Million w/ Severe Health Effects

## Slide 23: Non-Point Source Impacts
Importance

## Slide 24: Total Mercury in Mined vs. Unmined Streams
Rivers and Streams

## Slide 25: Methylmercury in Mined vs. Unmined Streams
Rivers and Streams

## Slide 26: Guadalupe River Watershed Mercury TMDL
1.5 ng/L in Water
0.05 mg MeHg/kg (Small Fish)
0.1 mg MeHg/kg (Big Fish)
Lakes

## Slide 27: Stratification of Lakes and Reservoirs
Ammonia
Sulfide
Phosphate
Manganese
Iron
Loss of cold-water habitat
Mercury

## Slide 28: Mercury in Aquatic Ecosystems
Enters System as Hg(II)
Converted to MeHg in Anaerobic Zones
Biomagnifies Up Food Web
Typically Associated with Eutrophic Systems
USGS

## Slide 29: How Lake Hg Enrichment Works
Mn(II)
Fe(II)
S(II)
Lakes
Oxycline

## Slide 30: Redox Chemistry of Oxygen Depletion
Hg Dynamics
SO42-
Fe3+ ← Mn3+
NO3- ← O2
+300 mV
+100 mV
Oxic
Anoxic
Anaerobic
Mn2+
S2- +
Fe2+
Hg2+
Fe3+
Mn3+
CH3Hg+
Hg2+, PO4, NH4+
Dominant Oxic Species
Sediment
Water Column
Hg2+
SRB
Adapted from Austin 2011

## Slide 31: Submerged Contact Chamber
Lakes

## Slide 32: Bubble Plume Oxygenation
Lakes

## Slide 33: Effects of Hypolimnetic Oxygen on Water Column Iron, Manganese, and Methylmercury
Lakes

## Slide 34: Bubble Plume Dynamics
Net Advective Flow Placement:
  Function of Flow per Lenth of Diffuser Line.
Mobley Engineering

## Slide 35: Targeting Oxygenation Zones in Upper Hypolimnion
Mobley Engineering

## Slide 36: Targeting Oxygenation Zones in Lower Hypolimnion
Mobley Engineering