## Slide 1: Review of Mixing Zone Studies
Ben Cope
EPA Region 10

## Slide 2: Science and Policy Intersection
Science
  e.g., data analysis, mixing theory, equations, model selection and results
Policy
  e.g., model inputs and associated assumptions, decisions related to narrative guidelines
  And obviously, final delineation of the mixing zone size/dilution

## Slide 3: Applicant Documentation
Detailed description of discharge
Detailed description of receiving water
MZ restrictions applicable to this discharge
Dilution model applied and why
Minimum dilution-with-distance table(s)
Model inputs/outputs attached to report
Model files shared with the agency

## Slide 4: Conservative assumptions are key
Must seek minimum dilution scenario
  Minimum flow in rivers
  Range of current speeds and stratification in marine waters (e.g., 10th and 90th percentiles)
  Range of effluent flow that includes maximum
  High end (e.g., 95th percentile) upstream/background concentration

## Slide 5: Dye Studies
Interesting real-world info, but…
Issue 1: Did study period represent critical conditions…i.e., minimum dilution?
  Likely not
  Models allow us to combine conservative assumptions
  They are reasonably well-tested tools
Issue 2: Did dye sampling hit the main plume?
Notes: Dye study result could trump model result if measured dilution is less than modeled minimum dilution
  Any examples of this out there?

## Slide 6: Agency responsibilities
Implementing all the narratives
Use of conservative dilution estimates
  Gives confidence that the actual radius of criteria exceedances will be equal or less than the authorized radius
Analysis of “applicant need” for dilution

## Slide 7: Two directions of analysis
Direction 1:
Start with allowable size based on state rules, determine dilution with distance using mass balance or model, and back-calculate the allowable effluent concentration.
1
Mixing zone extent defined upfront by regs
2
Volumetric dilution at edge of mixing zone
3
Dilution, background conc., and WQ criterion used to back-calculate limit

## Slide 8: …The other direction…
Direction 2
Start with the expected effluent concentration, determine dilution with distance using mass balance or model, and estimate the distance to point where the waste field is diluted to the standard.
3
Mixing zone extent defined by expected effluent and dilution
2
Accounting for background, determine distance from outfall where WQC are met
1
Expected discharge concentration identified
upfront