## Slide 2: PANTEX ENERGY RENEWABLE PROJECT(PREP) John M. Herrera PREP Contracting Officer Representative & Project Manager john.herrera@npo.doe.gov 806.477.4689

## Slide 3: Agenda
Pantex Plant Mission & Background
Federal Energy Goals
PREP Vision
Contract & Wind System Attributes
Project Management
R&D
PREP – Phase II

## Slide 4: Pantex Plant Mission
The Pantex mission is Securing America as the NNSA'S production integrator and provider of the nuclear deterrent to the Department of Defense.

## Slide 5: 1,500 Acres – Aerial View

## Slide 6: 1,500 Acres -Ground Level View

## Slide 7: Renewable Energy Requirements and Goals
  Federal gov’t to consume 7.5% renewable electric energy beginning FY13. (Energy Policy Act of 2005). Increased to 20% by 2020.
  Half of annual renewable energy must come from “new” energy sources and agencies must implement renewable energy generation on federal property. (EO 13423)
  Each agency shall increase renewable energy use, implement projects on agency property, and reduce greenhouse gas emissions. (EO 13514)

## Slide 8: PREP Vision
Vision: Install wind energy system up to 80 MW nameplate capacity with Texas Tech University Public-Private Partnership.

## Slide 9: ESPC Contract Strategy
RFP: Design, install, operate 9.0 – 15 MW wind farm using FAA approved locations.
NNSA Firm Fixed Price ESPC Contract
Siemens Government Technologies, Inc. Contract signed May 10, 2013.
  $50.5M Contract Value
  18 year term

## Slide 10: Wind System Features
Siemens Government Technologies, Inc.
  11.5 MW system
    Five (5) 2.3 MW Siemens w/ 101 meter blades
    Five (5) yr full system warranty
    Five (5) yr maintenance w/ five (5) option years
  47,000 MWH/yr production
    Pantex Plant uses ~72,000 MWH/yr
      ~65% of plant load
  System life is 25 years

## Slide 11: Energy “Savings”
Expected Savings
  Yr(1): $1,768,907
  25 Yrs: $84.4M
    5% energy escalation
Cost Benefit: $84.4M – $50.5M = $33.9M

## Slide 12: Surplus Renewable Energy Credits
94,000 RECs/yr
  47,000 RECs/yr produced
  Double counting eligible (EPACT 2005)
Pantex 7.5% Requirement = 5,400 RECs
Pantex 20% Requirement = 14,400 RECs
Surplus RECs spread to NNSA complex

## Slide 13: Milestones
Milestone | Date
CD-0: Mission Need, Approved | April 2009
Qualifying Facility Designation | June 2009
CD-1: Approve Alternative Selection and Cost Range, Denied | April 2010
Energy Savings Performance Contract(ESPC) Acquisition Strategy Approved | June 2011
Federal Aviation Administration(FAA) Approved Five (5) 426 ft. Locations | April 2012
ESPC Request For Proposal Released | September 2012
Contract Award | May 2013
Operational | July 2014

## Slide 14: Project Management

## Slide 15: PREP Work Breakdown
PREP
Development
NEPA
FAA
Acquisition
Implementation
Interconnection
Physical
Utility Tariff
RFP Development
RFP Release
Selection
Investment Grade Data
Construction

## Slide 16: Project Management Structure
OnePREP Team
Champion
Design Engineering
System Engineering
Contracting
Utility Management
Consultant
Agency Attorney
Contracting Officer
B&W Pantex
Idaho National Labs
NPO Production Office
NREL

## Slide 17: Development
NEPA
Federal Aviation Administration Obstruction Evaluation
12 months of Investment Grade Data
  60m Met Tower

## Slide 18: Acquisition
Acquisition Strategy
RFP Development
Bidder Selection
  PREP Evaluation Factors
    Experience
    System Capability
      Understand Performance Modeling
    Management Capability

## Slide 19: Implementation
Construction
Physical Interconnection
Tariff Interconnection

## Slide 20: Physical Interconnection
System Impact Study
Facility Study
Install System Upgrades
Power Backfeed

## Slide 21: Tariff Interconnection
Xcel Energy Electric Tariff(s)
  From: Large General Services
  To:
    Large General Services
    Transmission Standby Service
    Purchase of Non-Firm Energy From Qualifying Facilities

## Slide 22: R&D Collaboration
Data Collection and Analysis – All raw data collected as part of the manufacture/developers data collection systems associated to the wind farm will be made available to the TTU.
Optimization Research - Perform various operational test and performance evaluations to investigate improving system production.
New Technology Development - Perform additional studies, equipment installation/testing, etc. to further the development of the wind farm and power generation.

## Slide 23: PREP Phase II - Additional 35MW
Additional 35MW East of 2373
FAA VOR approach removal
Request For Information (FY13)
Regulatory Study (FY14)
Acquisition Strategy (FY14)
Acquire & Construct (FY16)

## Slide 24: Questions?
John M. Herrera PREP Contracting Officer Representative & Project Manager john.herrera@npo.doe.gov 806.477.4689