## Slide 1: A Proposed Semi-Passive Treatment System At Remote AML Sites
by
Robert H. Lambeth, PE, PG, LHG & Gene Andrews, PE
Millennium Science & Engineering, Inc.
Spokane, Washington
EPA HARDROCK MINING CONFERENCE 2012
Denver, Colorado
April 3, 2012

## Slide 2: Problem: ARD discharging into a popular Wild & Scenic River floodplain Question: Can you build a minimal cost, walk-away treatment system that has no footprint, odor, maintenance, or power needs? Answer: It would be difficult! Or more precisely – NO!

## Slide 3: History & Description
Volcanogenic Massive Sulfide deposit
Active 1898-1942
Most production 1908-1916
13 Adits
2 Shafts
4 Levels below River
10,000 feet of workings

## Slide 4: Ground Level View of Site

## Slide 5
Aerial View of Site
Y
100 Yr. Flood Plain
River Level Adit

## Slide 6
Floodplain Looking West

## Slide 7: All Adits

## Slide 8: Adit Discharge

## Slide 9: Discharge Quality
Flow = 10 gpm
pH = 2.9 su
Al = 19 mg/L
As = 0.016 mg/L
Cu = 3.5 mg/L
Fe = 93 mg/L
Pb = 0.21 mg/L
Se = 0.03 mg/L
Zn = 18 mg/L

## Slide 10: Treatment Design Considerations
Limited access
No power
Adit frequently flooded
Entire valley is a floodplain
Visibility
Vandalism
No water availability

## Slide 11: Basic Treatment Options
Neutralization (mandatory)
  Within wetlands?
  Caustic?
  Lime?
Sludge handling
  Direct discharge?
  Settlement basin w/removal?
  Filtration w/removal

## Slide 12: Neutralization Discussion
Lime addition
  Denser sludge
  Lower cost
  Doesn’t freeze, but
  More maintenance
  Greater power requirements
Caustic addition (Preferred)
  Much easier and simpler to use
  Less power needs
  Lower maintenance

## Slide 13: Bench & Field Tests
Performed by Ionic Water Technologies, Inc., Reno, NV
8 gpd of 30% NaOH solution to pH 9
All metals but Al declined to criteria in effluent
Sludge passed TCLP, but leachate still exceeded some criteria
Paint filter test was not performed
This Should Work!

## Slide 14: Settlement Option Issues
Wetlands
  Would have to be in the floodplain
  Will 10 gpm sustain an adequate size system for the pH?
  Visible and subject to vandalism
Settlement basins
  Would have to be in the floodplain
  Visible and subject to vandalism
>> Sludge removal for both awkward and the disturbed sludge may not pass the Paint Filter Test<<

## Slide 15
Potential Locations
Y
100 Yr. Flood Plain
River Level Adit
?
?
?
??
??
?? = Treatment plant
? = Basins
? = Pipeline
?
?

## Slide 16: Alternative Proposal!
Concrete plug in adit
  Can create head!
  Stops inundation!
Treatment system underground
  Hides it!
  Protects it!
Treated effluent to fabric filters
  Contains sludge!
  Protects sludge from flooding!
Discharge to drainfield for polish and concealment!

## Slide 17: Sludge Disposal ?!?
Use multiple fabric filter tubes in series!
Containerize filter tubes in large garbage dumpsters!
Change out full filter tubes quickly!
Dispose in local landfill!
  The sludge passes TCLP!
  The sludge should pass the Paint Filter Test!
>>The landfill can still reject it!!<<

## Slide 18: Flowsheet

## Slide 19: In-Adit Design

## Slide 20: Pipe Detail

## Slide 21: Surface Plan View

## Slide 22: COSTS
Capital Cost = $1,900,000
Five Year Capital & Operating Cost = $2,828,000

## Slide 23: Closing
More treatment/pilot tests are needed!
This can be phased in!
This is just one more wrench in the ARD remedial toolbox!

## Slide 24: Comments? Questions? Sticker Shock?