## Slide 1: Mine Water Treatment Strategies at Resolution Copper Mining and the Eagle Project
Kennecott’s Eagle Development Project
Project Development and Implementation
Casey McKeon, Resolution Copper Mining, LLC Kristin Mariuzza, Eagle Development Project

## Slide 2: OVERVIEW
Project Introductions
Regulations that govern project design
Water Treatment Design
Water Management

## Slide 3
3 Confidential; © Copyright Protected
Resolution Copper Project Overview
Near Superior, Arizona
Adjacent to the Magma Mine (1911-1996)
Rio Tinto and BHP partnership
3rd largest undeveloped Cu resource in world
1.62 billion tonnes @ 1.47% Cu
>$5 billion investment
40-year mine life
Located in the Historic Pioneer Mining District
Notes: 3

## Slide 4: Resolution Copper Water Treatment
Required for dewatering old Magma Mine workings adjacent to new work areas
  Safety of shaft sinking-exploration activities
Historic Treatment (pre -1996)
  Onsite ponds
  AZPDES requirement only
Present Day
  Over 2.5 billion gallons to dewater (2008)
  New HDS treatment process: Lime (pH) and Soda Ash (prevent scaling)
  AZPDES and Aquifer Protection Permits (APP) for discharges and solids storage ponds
  Treats to Aquifer Quality Limits and surface water standards
  Reverse Osmosis required for gypsum removal if discharging to nearby creek
  Looked for alternative, beneficial use of water

## Slide 5: Water Treatment Objectives
Dewater existing underground copper mine
Beneficially use the treated water in a cooperative effort

## Slide 6
Goal: remove water from existing copper mine (2009)
RCM Copper Mine
RCM Pipeline
Beneficial Reuse Area

## Slide 7: Project Cooperators
Resolution Copper Mining, LLC (RCM)
  Supply water and support sampling efforts
New Magma Irrigation and Drainage District (NMID)
  Facilitate land access and communicate with RCM
  6 cooperating growers
University of Arizona (UA)
  Provide laboratory services and quality control of data
NewFields Agricultural & Environmental Resources
  Coordinate and conduct sampling and reporting efforts and facilitate grower communication

## Slide 8: 5,200 acres; 68+ fields

## Slide 9: Monitoring Approach
Sample Type |  | Sampling Frequency |  | 
 |  | Continuous | Monthly | Quarterly
Water | Grab |  | X | X
 | In Situ Probe | X |  | 
Soil | 0-12” & 12-24” sample depths |  |  | X*
Plant | Tissue |  |  | X*
Water probes measure pH, specific conductance and temperature
Water grab samples measure salinity and nutrient related constituents monthly.
Soil samples measure salinity and nutrient levels quarterly and metals annually.
Plant tissue samples measure salinity and nutrient levels quarterly, depending on crop growth cycles, and metals annually.

## Slide 10
Water Quality Website

## Slide 11: Web Mapping Application
Allows stakeholders to view Project data related to soil salinity
  View Project infrastructure
  View field information
  Access Project documents
  Chart trends for soil constituent
Facilitates rapid, visual representation of key constituents to ensure project goals concerning agricultural production are being met
Used frequently during grower meetings to spatially and temporally compare each growers data
  Intended to be made available to each grower once login information is established

## Slide 12: Web Mapping Application

## Slide 13: Results: Soil Salinity 0-12”
Crop productivity has not been impacted
Chart: ECe (dS/m)
| Alfalfa (Grower A) | Alfalfa (Grower B) | Cotton | Turf | Wheat | Bermuda | Barley
Q1 2009 | 1.11 | 0.91 | 2 | 4.77 | 1.39 | 0.72
Q2 2009 | 1.76 | 1.35 | 2.41 | 5.28 | 1.95 | 1.06
Q3 2009 | 2.14 | 1.46 | 2.47 | 6.69 | 2.01 | 0.85
Q4 2009 | 1.86 | 1.52 | 2.05 | 6.14 | 1.94 | 0.86
Q1 2010 | 1.1312 | 1.0516 | 1.9969 | 5.7808 | 0.6748
Q2 2010 | 1.4746 | 1.2469 | 1.644 | 5.2097 | 0.815
Q3 2010 | 1.4467 | 1.2188 | 2.0084 | 4.9772 | 0.7794
Q4 2010 | 3.5034 | 1.1957 | 1.644 | 5.296 | 1.7151 | 0.6048 | 2.1318
Q1 2011 | 1.5205 | 1.0786 | 1.8982 | 3.8305 | 1.2866 | 0.8922 | 1.475
Q2 2011 | 2.35 | 1.47 | 1.92 | 5.57 | 1.35 | 1.03 | 2.05
Q3 2011 | 1.94 | 1.61 | 2.45 | 4.86 | 1.72 | 0.69
Q4 2011 | 2.95 | 1.57 | 1.94 | 5.3 | 4.74

## Slide 14: Results: Dewatering, over 2B gallons to date

## Slide 15: Communication with Growers
Semi-Annual meetings with growers prior to
each sampling event
  Discuss field conditions and recent field
  operations
  Ensure all farm staff are aware of our activities
  Share data

## Slide 16: Results
Nutrient and metal levels for the water, soil and plant tissue samples have all fallen within acceptable, expected ranges.
Environmental health and agricultural productivity have remained unaffected.
Soil salinities (gypsum) have increased slightly, as expected, but have not affected crop yield.

## Slide 17: Lessons Learned
Daily communication is critical among all project stakeholders
Conservative sampling and irrigation efforts throughout the project have been helpful for tracking salinity trends
Consistency in the water treatment and regular communications have led to continued project success.

## Slide 18
Kennecott’s Eagle Development Project
Project Development and Implementation

## Slide 19: Located in the Upper Peninsula of Michigan Marquette County
Eagle
Michigan, USA

## Slide 20
3 April 2012
Presentation Title
20

## Slide 21
Source: Kennecott Eagle

## Slide 22
Mine Site Layout
North
underground ore body (6 acres)
ventilation raise and aggregate backfill site
surface facilities
underground decline to ore body
mine portal
site access road
surface road from portal to storage pad
Source: Kennecott Eagle
Salmon-Trout River

## Slide 24: Michigan’s Environmental Regulations
Part 31, Water Resources Protection, of PA 451, Natural Resources and Environmental Protection Act, of 1994.
        Part 22 Rules, Groundwater Quality
        Part 4 Rules, Water Quality Standards
        Part 8 Rules, Water Quality Based Effluent Limit Development
3 April 2012
Regulatory Drivers
Part 632, Nonferrous Metallic Mining Regulations, of PA 451, Natural Resources and Environmental Protection Act, of 1994.
  Covers all aspects of mining and includes EIA

## Slide 25: Michigan’s Environmental Regulations
3 April 2012
Regulatory Drivers
Part 632, Nonferrous Metallic Mining Regulations, of PA 451, Natural Resources and Environmental Protection Act, of 1994.
- Underground Dewatering
- Storm Water Runoff from Operations Area
- Temporary Development Rock Storage Area
  Industrial Landfill Equivalency
  Leachate Collection
  Geomembrane Cover
Waters that Receive Treatment at WTF
Not Treated at WTF
- Sanitary Wastewater
- Non-Contact Storm Water
Managing Water On Site

## Slide 26: Michigan’s Environmental Regulations
3 April 2012
Regulatory Drivers
Part 31, Water Resources Protection, of PA 451, Natural Resources and Environmental Protection Act, of 1994.
Water On Site Governed by:
- Part 22 Rules - Groundwater Quality
  Contact Water Basin Liner Design
  Basis of Design for Facility and Infiltration Gallery
  Water Discharge Application Requirements
- Part 4 Rules - Water Quality Standards
  Antidegradation - Best Technology in Process in Treatment for BCC Mercury
- Part 8 Rules - Water Quality Based Effluent Limits
  Low Level Metals – Designated Use Protection
Due to groundwater venting, the state agency applied surface water discharge requirements to the venting location (groundwater seeps).

## Slide 27: Final Agency Decisions
3 April 2012
Regulatory Drivers
Parameter | Eagle Permit Limit Monthly Average (ug/l) | Michigan Drinking Water Standard (ug/l)
Selenium | 5 | 50
Mercury | 0.0021 | 2
Copper | 10 | 1300
Ultimately, the State of Michigan issued a water discharge permit that included limits protective of both surface and ground water.
Compliance points are both groundwater and WTF effluent.
Comparison of select Permit Limits and Drinking Water Standards

## Slide 28: Water Treatment Facility Schematic
Facility rain/snow
Mine Inflow
Filtration
Groundwater Infiltration System
Metals Precipitation Process
Double Pass Reverse Osmosis
Recycle for Mine
350 gpm
permitted

## Slide 31
Questions are Welcome.
Thank You.